OPP Board Serial Interface
Interface Document

(Project: BrdSerIntf)

Project # : Not applicable
P/N: Not applicable
Rev 0.2

This program is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version.

This program is distributed in the hope that it will be useful, but WITHOUT ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for more details.

You should have received a copy of the GNU General Public License along with this program. If not, see <http://www.gnu.org/licenses/>.

	PREPARED:	APPROVAL: / LEAD ENGINEER	APPROVAL: / ENGINEERING MANAGER
NAME	Hugh Spahr
DATE

Revision History
Version	Primary Author(s)	Description of Version	Date Completed
0.1	Hugh Spahr	Initial version	11/08/13
0.2	Hugh Spahr	Added save/erase configuration	12/21/13

# Purpose
The OPP Board Serial Interface provides a description of the serial interface for the Open Pinball Project board serial interface. The serial interface document includes:
- Solenoid Driver Board (Product ID 1001)
- Input Board (Product ID 1003)
# Product Overview
BrdSerIntf contains the serial interface for OPP boards. This document describes the APIs
# Applicable Documents
None
# Terms, Definitions & Acronyms
API	Application Program Interface
EOM	End of Message (0xff)
ICD	Interface Control Document
OPP	Open Pinball Project
PWM	Pulse Width Modulation
# Serial Interface Overview
BrdSerIntf port is currently initialized to 19.2 kbps, 8, N, 1. During the setup, a command is sent to get an inventory of cards that are on the serial interface chain. The cards are daisy chained together in the same way that FDDI or token ring boards are linked together. The host sends to the first card receiver which transmits to the second card's receiver. This continues until the last card where a jumper is installed so that the transmitter of the last card is connected to the host receiver.

Each card is given an address which is automatically discovered during the setup command. The host uses the address to send individual commands to cards.

All commands use card addresses to indicate the destination of the command, and EOM to indicate the end of the command. The exception to this is the inventory command where cards receive the command, and wait to see the end of message. The card then inserts its address before the transmitting the EOM.

After the inventory command is run, the cards are configured. The host sends a configuration to each input and solenoid card. Once that happens, cards operate independently and do all of the real time processing themselves without the intervention of the host. The host only polls the cards to get status, such as if a solenoid input switch was activated.
## Addressing
The most significant four bits of the address indicate card type, while the least significant four bits of the address byte indicate the instance of the card. The first card starts from 0, and each card increases its address by one.

Solenoid cards have the most significant bits set to 0 (CARD_ID_SOL_CARD), while input cards have the bits set to 1 (CARD_ID_INP_CARD).

Examples:
First solenoid card:	0x00
Second solenoid card:	0x01
Fifth solenoid card:	0x04
First input card:	0x10
Second input card:	0x11
Fifth input card:	0x14
# Serintf.h
The serial interface file contains the structures used to interface with the solenoid driver boards and input boards. If programming using the C programming language, this file can be included to get the necessary defines.
/* Each command starts with the Card ID except for inventory and EOM. Next comes
 * the command, then any data.
 */
typedef enum
{
  RS232I_GET_SER_NUM = 0x00,
  RS232I_GET_PROD_ID = 0x01,
  RS232I_GET_VERS = 0x02,
  RS232I_SET_SER_NUM = 0x03,
  RS232I_RESET = 0x04,
  RS232I_GO_BOOT = 0x05,
  RS232I_CONFIG_SOL = 0x06, /* For each solenoid, CFG_SOL_TYPE,
        * Initial kick, and Duty Cycle.
        */
  RS232I_KICK_SOL = 0x07, /* Value, mask */
  RS232I_READ_SOL_INP = 0x08, /* Data */
  RS232I_CONFIG_INP = 0x09, /* For each input, CFG_INP_TYPE */
  RS232I_READ_INP_BRD = 0x0a, /* Data, data */
  RS232I_SAVE_CFG = 0x0b,
  RS232I_ERASE_CFG = 0x0c,
  RS232I_NUM_CMDS,

  RS232I_INVENTORY = 0xf0, /* Each card adds byte for card type */
  RS232I_EOM = 0xff,
} RS232I_CMD_E;

#ifndef RS232I_INSTANTIATE
 extern
#endif
const U8 CMD_LEN[RS232I_NUM_CMDS]
#ifdef RS232I_INSTANTIATE
 ={ 4, /* RS232I_GET_SER_NUM */ 4, /* RS232I_GET_PROD_ID */
    4, /* RS232I_GET_VERS */ 4, /* RS232I_SET_SER_NUM */
    0, /* RS232I_RESET */ 0, /* RS232I_GO_BOOT */
    24, /* RS232I_CONFIG_SOL */ 2, /* RS232I_KICK_SOL */
    1, /* RS232I_READ_SOL_INP */ 16, /* RS232I_CONFIG_INP */
    2, /* RS232I_READ_INP_BRD */ 1, /* RS232I_SAVE_CFG */
    1, /* RS232I_ERASE_CFG */
  }
#endif
;
/* Note: This is the length of the cmd excluding card ID and cmd */

typedef enum
{
  CARD_ID_CARD_NUM_MASK = 0x0f,

  CARD_ID_TYPE_MASK = 0xf0,
  CARD_ID_SOL_CARD = 0x00,
  CARD_ID_INP_CARD = 0x10,

} RS232I_CARD_ID_E;

typedef enum
{
  USE_SWITCH = 0x01,
  AUTO_CLR = 0x02,
} RS232I_CFG_SOL_TYPE_E;

typedef enum
{
  DUTY_CYCLE_MASK = 0x0f, /* lsb 4 bits are duty cycle */
  MIN_OFF_MASK = 0x70,
} RS232I_DUTY_E;
/* Min off time is 0-7 times the initial kick time. If initial kick
 * is 20 ms and min off is 5, the solenoid will be forced off for 100 ms
 */

typedef enum
{
  STATE_INPUT = 0x00,
  FALL_EDGE = 0x01,
  RISE_EDGE = 0x02,
} RS232I_CFG_INP_TYPE_E;
# Commands
The following section describes all the commands and gives examples.
## Get Serial Number, 0x00
CardAddr + 0x00 + Serial number (4 bytes)

Example: Host queries the third solenoid card (addr 0x02) for its serial number. The card responds with the serial number 0x01234567.

Command: 0x02 0x00 0x00 0x00 0x00 0x00 0xff

Response: 0x02 0x00 0x01 0x23 0x45 0x67 0xff
## Get Product ID, 0x01
CardAddr + 0x01 + Product ID (4 bytes)

Example: Host queries the first input card (addr 0x10) for its product ID. The card responds with its product ID of 1002 (0x000003ea).

Command: 0x10 | 0x01 | 0x00 | 0x00 | 0x00 | 0x00 | 0xff

Response: 0x10 | 0x01 | 0x00 | 0x00 | 0x03 | 0xea | 0xff
## Get Version, 0x02
Get the firmware version that is running on a card. The firmware version is broken into a byte representing the major version, minor version, sub version and engineering version.

CardAddr + 0x02 + Firmware Version (4 bytes)

Example: Host queries the third input card (addr 0x12) for its version number. The card responds that it is running version 1.5.6.0 (major version 1, minor version 5, subversion 6, and engineering version 0.

Command: 0x12 | 0x02 | 0x00 | 0x00 | 0x00 | 0x00 | 0xff

Response: 0x12 | 0x02 | 0x01 | 0x05 | 0x06 | 0x00 | 0xff.
## Set Serial Number, 0x03
CardAddr + 0x03 + Serial number (4 bytes)

Example: Host sets the serial number of the second solenoid card (addr 0x01) to 32 (0x20 in hex). If the serial number has already been set, the card responds with the current serial number of the card. If the serial number can be programmed, it responds with the serial number found in the command.

Command: 0x01 | 0x03 | 0x00 | 0x00 | 0x00 | 0x20 | 0xff

Response: 0x01 | 0x03 | 0x00 | 0x00 | 0x00 | 0x20 | 0xff
## Reset, 0x04
CardAddr + 0x04

Example: Reset the fifth input card (addr 0x14). This resets the card and an inventory command must be resent to reconfigure the card's address.

Command: 0x14 | 0x04

Response: No response since the card resets
## Go Boot, 0x05
CardAddr + 0x05

Example: Reset the first solenoid card (addr 0x00). This resets the card and keeps the card in the bootloader so that the card firmware can be updated.

Command: 0x00 | 0x05

Response: No response since the card resets. After the reset the card remains in the bootloader. Cards should only be updated when connected directly to a host without any other cards on a chain.
## Configure Solenoid Board, 0x06
CardAddr + 0x06 + Solenoid Parameters (8 sets of parameters, 3 bytes each or 24 bytes total)

Each solenoid is configured using three bytes. The first byte is the type of solenoid, either use the switch input (0x01, USE_SWITCH) or auto clear (0x02, AUTO_CLR). If the solenoid is configured to use the switch input, when the switch input is closed, the solenoid fires. If the solenoid is configured to auto clear, the host can kick the solenoid using the kick which is automatically cleared, and the solenoid can be kicked another time without sending the a command to clear the kick.

The second byte is the initial kick for the solenoid in milliseconds. If the initial kick is supposed to be 100 ms, the byte should be 0x64.

The third byte is broken into the duty cycle to “hold” the solenoid active, and the minimum off time. The period for the hold is 16 ms. The least significant four bits indicate the amount of “on” time during the 16 ms period. To keep the solenoid on for 50%, during the hold period, the four bits should be set to 0x08. This is 8 ms/16 ms or 50%. For 25% hold, set the value to 0x04. This is 4 ms/16 ms or 25%. The maximum hold strength is 87.5%.

The minimum off time is calculated using the least significant three bits of the most significant nibble of the third byte. ((3rd byte & 0x70) >> 4). These three bits are multiplied by the initial kick time to determine the minimum off time for the solenoid. If the solenoid is using the switch contact, and the initial kick time is 105 ms, and the minimum off time is 315 ms, and the duty cycle is 75%, the configuration bytes would be 0x01 0x69 0x3c.

Example: Configure the first solenoid card (addr 0x00). The first four solenoids are configured as flippers, the second two are configured as pop bumpers, and the last two are configured as VUKs. The flippers are configured with an initial kick of 48 ms and 25% hold. The pop bumpers have initial kicks of 48 ms and no hold. The VUK have initial kicks of 100 ms and no hold.

Command: 0x00 | 0x06 | 0x01 | 0x30 | 0x04 | 0x01 | 0x30 | 0x04 | 0x01 | 0x30 | 0x04 | 0x01 | 0x30 | 0x04 | 0x01 | 0x30 | 0x00 | 0x01 | 0x30 | 0x00 | 0x01 | 0x64 | 0x00 | 0x01 | 0x64 | 0x00

Response: The card removes the command from the communication stream.
## Kick Solenoids, 0x07
CardAddr + 0x07 + Solenoids To Kick (1 byte) + Mask (1 byte)

Command for the host to kick the solenoids. The solenoid bits are active high. The mask bits allow individual or groups of solenoids to be turned on and off. If the solenoid is configured to auto clear, after the solenoid kicks, the bit is automatically cleared so a second command isn't needed to kick it again.

Example: Kick the third solenoid card (addr 0x02). Turn on solenoid 1 and 2 and turn off solenoid 3.

Command: 0x02 | 0x07 | 0x06 | 0x0e
CardAddr + 0x08 + Data (1 byte)

Each solenoid card returns a byte listing if any new inputs have occurred since the last read input command. The command contains a blank data byte to be filled out by the card. Bits are numbered from right to left with bit 0 being 0x01.

Example: Read first solenoid card (addr 0x00). Returns that inputs occurred on solenoid 0, 4, 6, 7.

Command: 0x00 | 0x08 | 0x00

Response: 0x00 | 0x08 | 0xd1
## Configure Inputs Board, 0x09
CardAddr + 0x09 + Input Parameters (16 sets of parameters, 1 byte each or 16 bytes total)

Each input is configured using one byte. Switches are typically active low since the input line has a pull up resistor, and the switch connects the input to ground. STATE_INPUT returns the current value of the input. FALL_EDGE returns a single '1' with the read input board command when the input changes from a high to low value. The '1' is held until the input is read. The next read input will return a '0' unless the input transitions from low to high, then low again. RISE_EDGE returns a single '1' with the read input board command when the input changes from a low to high value. The '1' is held until the input is read. The next read input will return a '0' unless the input transitions from high to low, then high again.

Example: Configure the first input card (addr 0x10) with the first 8 inputs as STATE_INPUTS, next 4 inputs as FALL_EDGE, and last four inputs as RISE_EDGE.

Command: 0x10 | 0x09 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x00 | 0x01 | 0x01 | 0x01 | 0x01 | 0x02 | 0x02 | 0x02 | 0x02

Response: The card removes the command from the communication stream.
## Read Input Board Inputs, 0x0a
CardAddr + 0x0a + Data (2 bytes)

Each input card returns two bytes listing the state, or if a transition has occurred since the last read input command. The command contains two blank data bytes to be filled out by the card. Bits are numbered from right to left with bit 0 being 0x00 0x01, and bit 15 being 0x80 0x00.

Example: Read first input card (addr 0x10). Returns that inputs occurred on inputs 0, 5, 6, 7, 9, 10 and 15.

Command: 0x10 | 0x0a | 0x00 | 0x00

Response: 0x10 | 0x0a | 0x84 | 0xe1
## Save Cfg, 0x0b
CardAddr + 0x0b

Save the current configuration to the card. The next time the card is powered, it will automatically be configured without need another configuration command.

Example: Save the configuration to the first solenoid card (addr 0x00)

Command: 0x00 | 0x0b

Response: The card removes the command from the communication stream.
## Erase Cfg, 0x0c
CardAddr + 0x0c

Save the saved configuration. The next time the card is powered, it will need to be configured. Note: This command does not disable the current configuration.

Example: Erase the configuration to the first input card (addr 0x10)

Command: 0x10 | 0x0c

Response: The card removes the command from the communication stream.
## Inventory Command, 0xf0
The inventory command is used to figure out the number of cards and the position of the cards. When a card receives the inventory command, it listens and remembers the card addresses which match its card type. When it receives the end of message, it inserts its card address and increments the last matching card type address that it saw.

Example: Send the inventory command and find out that there are two solenoid cards, and one input card. The input card is the second card in the chain.

Command: 0xf0 | 0xff

Response: 0xf0 | 0x00 | 0x10 | 0x01 | 0xff
## End of Message, 0xff
End of message is needed at the end of an inventory command. It can also be used at the end of any command chain.
# Board Connector Positions
## Input Board

## Solenoid Board

## RS232 Interface

# Appendix